Proposed Town of Waterboro Driveway Ordinance

Driveways

Section 1 Applicability:

Section 1 of this ordinance shall apply to all driveways/entrances within the Town of Waterboro.  All references to the term “driveways” shall apply to all new driveway/entrance access and change of use as defined in this ordinance.

Definitions:

Driveway:  This ordinance shall apply to all private driveways within the Town of Waterboro. All references to the term “private driveway” shall be deemed to apply to a new driveway access to a single family residence, a duplex, or a commercial or institutional entrance in conjunction with site plan review and subdivision regulations.

Change of Use:  Any change of use of a single family, multi-family (or more) housing unit or commercial use.

Travel way:  Portion of the road in which an automobiles drives on.

Shoulder: Is a gravel or grass area adjacent to the travel way and paved shoulder (where applicable).

The provisions contained in Section 1 shall only apply to the intersection of the driveway/ entrance/change of use with the street that it provides access to for a distance of thirty (30’) feet from the travel way.

This ordinance shall take effect upon approval by the Town of Waterboro.  Once approved, this ordinance will override any previous ordinance.

Section 2 Driveways:

All new driveways/entrances /change of use proposed to be constructed within the Town of Waterboro shall be required to meet the provisions of this Ordinance.

Section 3 Application Procedures:

The procedure for application for proposed new driveways/entrance/change of use shall be as follows:

- Prior to the construction of any new driveway/entrance/change of use of an existing driveway/entrance, a completed application shall be submitted to the Code Enforcement Office on forms approved by the Town. The application shall include the following information:

- Name(s) of applicant(s) with a home/business address and phone number.

- Owner(s) of the land and the map/lot and address of the proposed new driveway/entrance/change of use.

- A statement of any legal encumbrances on the land for the location of a proposed driveway/entrance/change of use.

- All driveway/entrances/change of use permits shall be submitted with a dig safe #

- The anticipated starting and completion date of construction.

B. Drawings of the proposed driveway/entrance/change of use shall be submitted to the Code Enforcement Office with the application. The drawings shall include all of the following information.

- Date, scale (no less than 1” = 30 feet), name of street the driveway/entrance/change of use is going onto and the speed limit of the road.

- Intersection of the proposed driveway/entrance/change of use with an existing public street and their location and relationship with respect to any existing natural waterways in the vicinity of the proposed driveway/entrance/change of use.  Any driveway not built to these standards on a private road and requested to become a town road shall be reason for non-acceptance of said road.

- Approximate centerline gradients of the proposed driveway/entrance/change of use within thirty (30’) feet of the travel way of the existing street.

- Locations of existing overhead and underground utilities including, but not limited to, water, sewer, electricity, telephone, lighting, and cable television with the pole number indicated on the sketch.

C. The fee schedule for review of plans for a new driveway/entrance or an alteration to an existing driveway/entrance shall be established by the Board of Selectmen.

D. Building permits that are associated with any new construction of driveways/entrances shall not be issued until the Code Enforcement Office has determined that the applicant’s driveway/entrance construction application is complete and has been approved in accordance with the following provisions:

- All applications for driveway/entrance/change of use permits for access to streets and street turnarounds owned and/or maintained by the Town of Waterboro shall be subject to review for approval or denial within ten (10) business days by the Public Works Director. The Public Works Director shall also review driveways/entrances/change of use to be located on street turnarounds to ensure that snow plowing operations are not hindered.

- In the event that a proposed driveway/entrance/change of use is located such that the Code Enforcement Officer and/or Public Works Director determine that the input of a professional engineer is needed to verify compliance with the driveway performance standards of this ordinance, a review by a licensed Engineer may be requested by the Town Officials, and the costs of that review shall be paid by the applicant(s).

- All new subdivision plans shall have all driveway entrances shown to scale and must meet all requirements of this ordinance.

A separate driveway permit shall not be required for all driveways shown on approved subdivision plans which have been approved by the Public Works Director before final plan approval is given by the Planning Board. Changes to the design are allowed subject to the submittal of a completed driveway permit application to Public Works Director/Code Enforcement Officer and if in determination of the Public Works Director/Code Enforcement Officer a licensed Engineer is needed, the applicant shall bear all costs.

Section 4: Driveway Layout and Construction:

A. All new driveways/entrances/change of use constructed after the date of adoption of this ordinance shall meet the driveway construction standards of Table 1.

| Table 1: Driveway Required Construction Standards |
| --- |
| Maximum grade w/in 30 feet of street travel way surface residential | 5% (positive or negative grade) |
| Minimum angle of intersection with street | 75 degrees |
| Maximum angle of intersection with street | 105 degrees |
| Minimum diameter of culverts at intersection | 15 inches |

- All new driveways/entrances/change of use shall be located such that vehicles approaching or using the entrance will be able to obtain adequate sight distance in both directions along the street or to maneuver safely and without interference with traffic in accordance with the following provisions:

- Measurements to determine sight distance shall be made in the proposed driveway/entrance/change of use at a point seventeen (17’) feet from the centerline of the paved road or if not paved seventeen (17’) feet from the centerline of the travel way with the height of eye three and one-half (3.5’) feet above the pavement. The sight distance shall be computed from this point measuring along the roadway to a point where an approaching height of object four and one quarter (4.25’) feet is first seen.

- Driveway/entrance/change of use placement shall be such that an exiting vehicle has an unobstructed sight distance in both directions meeting the requirements of Table 2 unless a waiver is granted by the a licensed Engineer upon documentation provided by the applicant that safety conditions will be met with shorter sight distances (this review will be covered by the Town requirements).

Commercial driveway entrances and exits not serving traffic of over fifteen percent (15%) truck traffic shall meet the Mobility Sight Distance requirements of Table 2 (third column).

| Table 2: Driveway Entrance Sight Distance Standards |
| --- |
| Posted Speed (MPH) | Sight Distance (Feet) | Mobility Sight Distance (1) |
| 20 | 155 | 225 |
| 25 | 200 | 300 |
| 30 | 250 | 380 |
| 35 | 305 | 480 |
| 40 | 360 | 580 |
| 45 | 425 | 710 |
| 50 | 495 | 840 |

An applicant may ask for a sight distance waiver when special conditions exist.  The following steps will be required before any waiver will be considered.

- A study and plan by a traffic engineer.

- All costs will be borne by applicant(s) any requirements deemed necessary by said traffic Engineer shall be borne by the applicant(s).

- Driveways/entrances/change of use accessing State Highways or State Aid Highways shall require an MDOT entrance permit as a precondition for a permit from the Town of Waterboro.

D. 	All driveways/entrances/change of use shall have drainage facilities that have the appropriate capacity to provide for adequate removal of storm water to prevent flooding and erosion:

1. Culverts shall be new and of adequate size (minimum size) and depth to convey ditch water flows and shall be shielded with stone rip rap or a concrete header at inlet and outlet to prevent washouts when the ditch flow capacity is exceeded in major storms.  Minimum culverts shall be 15” x 32’.  Culverts types shall be: CMP (corrugated metal ) aluminized type 2 coated, galvanized type 2 coated, reinforced concrete pipe (RCP), plastic pipe end 12 smooth bore construction grade.

2. Surface drainage shall be provided so that all surface water on the new driveway/ entrance/change of use shall be carried away from the roadway. The driveway/entrance/change of use surface shall slope away from the road at a rate of not less than one quarter inch (.25”/ft.) per foot, nor more than one inch (1”/ft.) per foot for a distance of not less than the prevailing width of the existing shoulder, but in no case less than four (4’) feet from the edge of the travel way surface.

E. 	Driveways/entrances/change of use shall be located not less than fifty (50’) feet from the tangent point of the travel way edge radius of any intersection of streets. Two (2) driveways shall not be located across from each other.

F. 	When a corner lot is bounded by streets of two different classifications, driveways/entrances/change of use to the corner lot shall gain access from the street of lower classification unless, in the opinion of a licensed Engineer, if there is good reason to do otherwise (e.g., on the higher classification road the driveway/entrance/change of use can be located more safely from the intersection and sight distances can be improved).  The final decision shall rest with the Public Works Director.

G. 	There shall be a minimum turning radius of ten (10’) feet at the intersection of a driveway/entrance/change of use with the street. If necessary, the width of the travel way of the driveway/entrance/change of use shall be increased in the vicinity of the intersection to provide for this turning radius. Commercial driveway entrances and exits needing site plan review and under subdivision regulations serving traffic of over fifteen percent (15%) truck traffic shall be designed with adequate width to avoid a turning vehicle from tracking into the opposing travel lane.

H. 	Driveways/entrances/change of use shall be located so that the edge of the shoulder closest to a property line is at least five (5’) feet from that property line unless the following conditions are met for a driveway/entrance/change of use shared between abutting properties.  This applies to driveways/entrances/change of use built after the enactment of this ordinance.

1. The driveway shall have a minimum travel way width of twenty four (24’) feet for the first thirty (30’) feet before dividing into separate driveways.  This shall apply for single family and two (2) family common driveways.  Driveways serving more than two (2) single family homes shall be reviewed by the Public Works Director to determine what additional requirements shall be met.

2. Deeded rights to the driveway/entrance/change of use shall be issued for both lots serviced by the common driveway/entrance and a maintenance agreement specifying rights and responsibilities for its maintenance signed by the parties shall be filed with the driveway permit application and recorded at the York County Registry of Deeds.

Section 5 Temporary Driveways:

- Temporary driveways/entrances/change of use shall be allowed for temporary use only when no building permit is to be issued.  An example would be wood lot cutting, road construction and similar uses.

- Temporary driveways/entrances/change of use shall be allowed when a building permit is needed if in the determination of the Public Works Director that a construction entrance would better serve the site and create a safer entrance or damage to the permit entrance is possible.

- All temporary entrances shall be constructed to a minimum standard of 100 feet (100’) long and 25 feet (25’) wide with 8 inch (8”) minimum of 1 ½ inch (1.5”) stone. The entrance must be approved by the Public Works Director before construction on the site shall commence.

- Temporary entrances shall be good for a period of six (6) months with one (1) six (6) month renewal.  If additional time is needed, it will be up to Public Works Director and the Code Enforcement Officer to extend beyond three hundred sixty five (365) days.  Removal of temporary entrances must be completed within sixty (60) days of termination of use of said temporary entrance.  And within ninety (90) days the areas must be returned to original configuration (loamed & seeded where necessary) and have a 90% grass catch or meet site plan approved design or engineered specifications.  Erosion control materials may be used where necessary in lieu of sod, grass or other growth materials.

- When sight distance is inadequate, special requirements must be met.  This may require signage, flaggers and adequate warning lights during working hours.  Signage shall be determined by the Public Works Director.  Cost of temporary signage shall be borne by the applicant(s) and installed by the Town of Waterboro.

Any dispute that arises between the applicant(s) and the town of Waterboro shall be appealed to the Zoning Board of Appeals.